## Slide 1
*.rzone (optional) that defines System Resources
*.csolution.yml Defines Target Application
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
that defines Device Properties
Board Support Pack (BSP) that defines Board Properties
CMSIS Project Manager
Project Files *.cprj for CMSIS Build
User Input Files
Software Packs
[default.]csettings.yml Global Settings (Toolchain, Device)
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
Output Files

## Slide 2
Read previous *.cprj files to check for config file version changes
Control config file versions in case of updated software packs
Read Software Packs and User Input Files
Process data
Read previous *.cprj file to identify the config file versions previously used
Compare versions of “config” files, notify if updates are made (define rename process of config files)
Check if new *.cprj file is different from old config files; if it differs rename existing *.cprj to backup version; write new *.cprj file
Q: do we need a status file, perhaps for an IDE flow?
*.rzone (optional) that defines System Resources
*.csolution.yml Defines Target Application
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
that defines Device Properties
Board Support Pack (BSP) that defines Board Properties
CMSIS Project Manager
Project Files *.cprj for CMSIS Build
User Input Files
Software Packs
[default.]csettings.yml Global Settings (Toolchain, Device)
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
Output Files

## Slide 3: Application Software – from Virtual to Physical Hardware
User Application Code
Virtual Layer
IoT/ML Software Platform
Provide evidence of correctness on Arm Virtual Hardware Target and Physical Hardware
Event Log file
User Application Code
Board Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
Virtual Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing on Virtual Hardware or Physical Hardware Boards
Deployment and System Testing on Production Hardware
Essentially the same event logs are generated across the different deployments. This ensures correctness.
Simulated I/O via Python scripts and stimuli files
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 4: Multi-Project Requirements
Project D
Project B
Project A
Separate projects independently developed; combined in a multi-project workspace
Security
Storage
Crypto
Attestation
Device / Board HAL
RTOS
User Application
Cloud
Connector
Secure Network
Interface
Secure Boot
ML Library
ML Data
UX Graphic
Images
Control Algorithm
Processor #1
Processor #2
Project C